## Slide 1
Accurate Predictions of Genetic Circuit Behavior from Part Characterization and Modular Composition
Jacob Beal, Noah Davidsohn, Aaron Adler, Fusun Yaman, Yinqing Li, Zhen Xie, Ron Weiss
5th IWBDA
July, 2013

## Slide 2: EQuIP: Realizing the Dream
TAL14
Active pop. mean MEFL vs time
TAL14-TAL21
Precise Match!

## Slide 3: Outline
Calibrating Flow Cytometry TASBE Method
Building EQuIP Models
Prediction & Validation
[Beal et al., Technical Report: MIT-CSAIL-TR-2012-008, 2012]

## Slide 4: First, some metrology…
Unit mismatch!
Output
[R2]
[R1]
[Output]
[R2]
R2
R1
Arbitrary Red
Arbitrary Blue
Arbitrary Red
Arbitrary Blue

## Slide 5: How Flow Cytometry Works
Challenges:
Autofluorescence
Variation in measurements
Spectral overlap
Time Contamination
Lots of data points!
Different protein fluorescence
Individual cells behave (very) differently

## Slide 6: Fluorescent Beads  Absolute Units
Run beads every time: flow cytometers drift up to 20 percent!
Also can detect instrument problems, mistakes in settings
SpheroTech RCP-30-5A

## Slide 7: Compensating for Autofluorescence
Negative control used for this

## Slide 8: Compensating for Spectral Overlap
Strong positive control used for each color
Note: only linear when autofluorescence subtracted

## Slide 9: Translating Fluorescence to MEFL
Only FITC channel (e.g. GFP) goes directly
Others obtained from triple/dual constitutive controls
Must have exact same constitutive promoter!
Must have a FITC control protein!

## Slide 10: Outline
Calibrating Flow Cytometry
Building EQuIP Models
Prediction & Validation
EQuIP = Empirical Quantitative Incremental Prediction

## Slide 11: TASBE Characterization Method
Transient cotransfection of 5 plasmids
Calibrated flow cytometry
Analysis by copy-count subpopulations
Output
Dox
R1
pCAG
Dox
T2A
rtTA3
VP16Gal4
pTRE
EBFP2
pTRE
R1
pUAS-Rep1
EYFP
pCAG
mkate
pCAG

## Slide 12: Multi-plasmid cotransfection!?!
Avoids all problems with adjacency, plasmid size, sequence validations
Variation appears to be independent

## Slide 13: Result: Input/Output Relations
R1 = TAL14
R1 = TAL21
Transfer curve for TAL 14
Transfer curve for TAL 21

## Slide 14: Expression Dynamics
Fraction Active
Mean Expression
Results  division rate, mean expression time, production scaling factor

## Slide 15: EQuIP model
Model = first-order discrete-time approximation
O(t)
P(I,t)
+
Delay
I(t)
Dilution
& decay

## Slide 16: Outline
Calibrating Flow Cytometry
Building EQuIP Models
Prediction & Validation

## Slide 17: EQuIP Prediction
pCAG
Dox
T2A
rtTA3
VP16Gal4
pTRE
EBFP2
pTRE
R1
pUAS-Rep1
pUAS-Rep2
EYFP
R2
pCAG
mkate
pCAG
R2
Output
Dox
R1
O(t)
P(I,t)
+
Delay
I(t)
Dilution
& decay
P(I,t)
+
Delay
Dilution
& Decay
R1 Device
R2 Device
+

## Slide 18: Incremental Discrete Simulation
[TAL21]
[TAL14]
[OFP]
TAL14
OFP
TAL21
state
TAL14
production
TAL14
state
OFP
production
OFP
state
time
hour 1
hour 2
hour 46
loss
production
production
loss
production
+
-
+
+
+
+
+
-
…
-
-
-
…
-
…

## Slide 19: High Quality Cascade Predictions
TAL14  TAL21
TAL21  TAL14
Circles = EQuIP predictions
Crosses = Experimental Data
1.6x mean error on 1000x range!

## Slide 20: Contributions
TASBE method calibrates flow cytometry data
Cotransfected test circuits give good models
EQuIP accurately predicts cascade behavior from models of individual repressors
Now for bigger, better circuits on more platforms…

## Slide 21: Acknowledgements:
Aaron Adler
Fusun Yaman
Ron Weiss
Noah Davidsohn
Yinqing Li
Zhen Xie

## Slide 22: Characterization Tools Online!
https://synbiotools.bbn.com/